## Slide 1: Computer Organization & Assembly Language
Lecture 4

## Slide 2: Airthmetic Instructions
Addition
  ADD destination, source (destination operand can be register or memory)
  ADC destination, source (source can be register, or in memory, or immediate)
Example
  MOV AL, 3FH
  MOV BH,23H
  SUB AL,BH ; subtract BH from AL, Place result in AL
  SBB AL, 0

## Slide 3: SUBTRACTION
Subtraction
  SUB destination, source (destination operand can be register or memory)
  SBB destination, source (source can be register, or in memory, or immediate)
Example
  MOV AL, 0F5H
  ADD AL,0BH ; AL becomes 00
  ADC AL, 0

## Slide 4: Logic Instructions
To manipulate individual bits
Binary Value 0 treated as false
Binary Value 1 treated as true
In Assembly Language:
  AND
  OR
  XOR
  NOT
  TEST

## Slide 5: Truth Tables
a | b | a AND b | a OR b | a XOR b
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0
a | NOT a
0 | 1
1 | 0

## Slide 6: Examples
1010 1010 AND 1111 0000 = 1010 0000
1010 1010 OR 1111 0000 = 1111 1010
1010 1010 XOR 1111 0000 = 0101 1010
NOT 1010 1010 = 0101 0101

## Slide 7: Syntax
AND destination, source
OR destination, source
XOR destination, source
Destination:
  Stores result
  Can be Register or Memory Location
Source:
  May be a Constant, Register or Memory Location
Memory to memory operation not allowed

## Slide 8: MASK
To modify only selective bits in destination, we construct a source bit pattern known as MASK.
To choose mask, use following properties:
  b AND 1 = b
  b AND 0 = 0
  b OR 1 = 1
  b OR 0 = b
  b XOR 0 = b
  b XOR 1 = ~b (complement of b)
  Where b represents a bit (0 or 1)

## Slide 9: Contd..
1. The AND instruction:
- May be used to clear specific destination bits while preventing the others.
- A 0 mask bit clears the corresponding destination bit.
- A 1 mask bit preserves the corresponding destination bit.

## Slide 10: Example 1
Clear the sign bit of AL while leaving the other bits unchanged.
Solution:
AND AL, 7Fh
Where 7Fh (0111 1111) is the mask.

## Slide 11: Contd..
2. The OR instruction:
- May be used to set specific destination bits while preventing the others.
- A 1 mask bit sets the corresponding destination bit.
- A 0 mask bit preserves the corresponding destination bit.

## Slide 12: Example 2
Set the MSB and LSB of AL while preserving the other bits.
Solution:
OR AL, 81h
Where 81h (1000 0001) is the mask.

## Slide 13: Contd..
3. The XOR instruction:
- May be used to complement specific destination bits while preventing the others.
- A 1 mask bit complements the corresponding destination bit.
- A 0 mask bit preserves the corresponding destination bit.

## Slide 14: Example 3
Change the sign bit of DX.
Solution:
XOR DX, 8000h
Where 80h (1000 0000) is the mask.

## Slide 15: NOT Instruction
Performs the one’s complement operation on the destination.
Syntax:
NOT destination
No effect on flags
Example: Complement the bit in AX:
NOT AX

## Slide 16: Multiplication
MUL instruction is used with unsigned operands
Unsigned multiplication of 128 and 255 = 32, 640.
2 bytes multiplied, product = 1 word (16 bits)
  AL is implied destination operand
  Source operand can be a register or variable (8 bits)
  16-bit output is AX
2 words multiplied, product = 1 double word (32 bits)
  AX is implied destination operands
  Source operand can be a register or variable (16 bits)
  32-bit output is DX:AX

## Slide 17: MUL Instruction
8-bit multiplication:
MUL BL ; product = AX
16-bit multiplication:
MUL DX ; product = DX:AX
mov al,5
mov bl,10h
mul bl ; AX = 0050h
mov ax,500h
mov bx,100h
mul bx ; DX:AX = 00050000h

## Slide 18: DIV Instruction
Dividend is divided by divisor
Result: Quotient and Remainder
Byte Form:
  Dividend is AX
  Divisor can be 8-bit register or variable
  Quotient is AL, Remainder is AH
Word Form:
  Dividend is DX:AX
  Divisor can be 16-bit register or variable
  Quotient is AX, Remainder is DX
Status flag values are undefined

## Slide 19: DIV Examples
mov ax,0083h ; dividend
mov bl,2 ; divisor
div bl ; AL = 41h, AH = 01h
mov dx,0 ; dividend, high
mov ax,8003h ; dividend, low
mov cx,100h ; divisor
div cx ; AX = 0080h, DX = 0003h

## Slide 20: Divide Overflow
Happens when the quotient is too large to fit in the destination register. Causes a processor interrupt.
mov dx,0050h ; dividend, high
mov ax,0000h ; dividend, low
mov cx,10h ; divisor
div cx ; quotient= 50000h, cannot ; fit in AX register

## Slide 21
Carry flag
Parity flag
Auxiliary flag
Zero
Overflow
Direction
Interrupt enable
Trap
Sign
6 are status flags
3 are control flag
Flags

## Slide 22: The Status Flags
1. Carry Flag:
  Carry Flag is set to 1 when there is an unsigned overflow. For example, when you add bytes 255 +
  1 (result is not in range 0…255). When there is no overflow, this flag is set to 0.Examples:
  The Carry Flag is set to 1 when there is a carry out from MSB on addition or there is a borrow into the MSB on subtraction. Also affected by shift and rotate instructions.
  0FFh + 11h = 110h (If a register can store only 1 byte, then where to store the carry generated by MSB?)
  1000 0001b – 1000 0010b = 11111111b (How processor would know a borrow is required to perform subtraction?)

## Slide 23: Contd..
2. Parity Flag:
  Parity Flag is set to 1 when there is even number of ones in result, and to 0 when there is odd number of ones.
  PE (Even Parity): If the byte of a result has even number of one bits. For Even parity, PF = 1
  PO (Odd Parity): If the byte of a result has odd number of one bits. For Even parity, PF = 0
  Examples:
  1000 0001b – 1000 0010b = 11111111b (Number of one’s in result = 8, so PF = 1)

## Slide 24: Contd..
3. Auxiliary Carry Flag:
  Auxiliary Flag is set to 1 when there is an unsigned overflow for low nibble (4 bits).
  The Auxiliary Carry Flag is set to 1 if there is a carry out from bit 3 on addition, or a borrow into bit 3 on subtraction.
  Used in Binary Coded Decimal (BCD) Operations.
  Examples:
  1000 0001b – 0000 0010b = 01111111b (Borrow from bit 4 to bit 3)

## Slide 25: Contd..
4. Zero Flag:
  Zero Flag is set when the result is zero.
  Zero Flag is unset when result is non zero.
  Examples:
  0FFh – 0FFh = 00h

## Slide 26: Contd..
5. Sign Flag:
  Sign Flag is set to 1 when result is negative. When result is positive it is set to 0. This flag takes the value of the most significant bit.
  Examples:
  0FFh – 0FFh = 00h (MSB = 0, PF = 0)

## Slide 27: Contd..
6. Overflow Flag:
Overflow:
  Range of numbers that can be represented in a computer is limited.
  Overflow Flag is set to 1 when there is a signed overflow. For example, when you add bytes 100 + 50 (result is not in range -128…127).
Same signs → result has different sign | OF = 1 (overflow occurred)
Different signs → result has same sign as one operand | OF = 0 (no overflow)

## Slide 28: Example 1 – overflow occurs
0110 0000 (+96)
+ 0100 0110 (+70)
-------------
1010 0110 (-90) ❌ wrong sign → overflow
Both operands were positive, but result is negative (MSB = 1). ✅ Overflow Flag = 1

## Slide 29: Example – 2 No Overflow
1001 0000 (-112)
+ 1110 0000 (-32)
-------------
0111 0000 (+112) ❌
wrong sign → overflow
Both operands were negative, but result is positive → OF = 1
0110 0000 (+96)
+ 1110 0000 (-32)
-------------
0100 0000 (+64) ✅
correct sign → no overflow
Operands have different signs, so overflow cannot occur → OF = 0

## Slide 30: MUL (Flags)
Carry and Overflow flags are set when the product extends into its high register:
mov ax,5000h
mov bx,10h
mul bx ; DX:AX = 00050000h
; CF=1, OF=1
mov ax,500h
mov bx,10h
mul bx ; DX:AX = 00005000h
; CF=0, OF=0

## Slide 31: Variables In Emu8086
Variable is a memory location. For a programmer it is much easier to have some value be kept in a variable named "var1" then at the address 5A73:235B, especially when you have 10 or more variables.
name DB value name DW value DB - stays for Define Byte. DW - stays for Define Word.
name - can be any letter or digit combination, though it should start with a letter. It's possible to declare unnamed variables by not specifying the name (this variable will have an address but no name).
value - can be any numeric value in any supported numbering system (hexadecimal, binary, or decimal), or "?" symbol for variables that are not initialized.

## Slide 32
VAR1 DB 7
var2 DW 1234h
MOV AL, var1
MOV BX, var2